## Slide 1: 폐기능검사 How to do and interpret?
고신대학교 의과대학 호흡기내과 옥철호

## Slide 2: Contents
Brief history of spirometry
Introduction of parameters in Pulmonary function test.
Acceptance and Reproducibility in PFT
Examples and interpretation of airway obstruction in PFT
Simple Spirometry in primary clinic or home.

## Slide 3: 폐기능검사의 기원

## Slide 4: In the beginning of Spirometry
in the 1840’s by John Hutchinson an English surgeon.
The volume of exhaled air from fully inflated lungs could accurately be measured by exhaling into a water tube leading into the bucket:
classic water type spirometers

## Slide 5: Origin of The Term “Vital Capacity”
the term “vital capacity”, capacity for life, used primarily in a limited function to measure usable lung volumes in patients at tuberculosis sanitariums.

## Slide 6: Vital Capacities Forced Vital Capacity
Interstitial lung disease TB destroid lung Fibrothorax

## Slide 7: The limitation of First Spirometry
90% of the predominant respiratory disorders (asthma and COPD) were obstructive (limited flow rate) in nature whereas vital capacity measured restriction.
In 1950 Dr. Tiffeneau of France introduced the forced measurement of air volume during a given time frame, i.e., forced expiratory volume in 1 second, FEV1.
vital capacity

## Slide 8: Renovation of Second Spirometry
the classic water type spirometers were not suitable for accurately measuring flow rates.
In 1960, the first available waterless spirometer providing an easier, more accurate, hygienic and affordable spirometer – early detection of pulmonary disease at the physician office level.

## Slide 9: 용어 정리
1초 노력 호기량
노력 폐활량
노력 호기 중간기류량: 호기근의 노력과 관련없는 초기의 소기도 변화
1초율

## Slide 10: 1초당 노력 호기량 FEV1

## Slide 11: Vital Capacity and FEV1

## Slide 12: 4차 산업 혁명 기반 개인용 사물 ICT 의료기기 Smart city: 개인정보 규제 완화 지역
1.2,3 차 진료 의료기관을 이용객의 개인정보를 서로 공유

## Slide 13: SPIROMETRY : 폐기능검사

## Slide 14: 1초당 노력 호기량 FEV1

## Slide 15: COPD 환자에서 폐기능검사가 필요한가?

## Slide 16: 폐기능 검사 하면 좋은데…….
“결핵및호흡기학회가 10년 이상 흡연 병력이 있는 40세 이상 1차 의료기관(동네의원) 진료 경험이 있는 환자를 대상으로, 기침·호흡곤란·가래 중 하나의 증상만 있어도 대학병원에서 폐기능 검사를 한 결과 대상자의 23%가 COPD 환자였다
폐암의 의료.사회비용 2조, 천식 4조, COPD 1.7조

## Slide 17: 폐기능검사를 통한 airflow 중증도 확인

## Slide 18: COPD의 유병율과 예후

## Slide 19: 노력 호기 중간기류량 FEF 25-75% COPD 예측 및 추후 경과 관찰
호기근의 노력과 관련 없는 초기의 소기도 변화

## Slide 20: 폐기능 검사

## Slide 21: 검사의 적절성
끝이 뽀족해야함

## Slide 22: 폐기능 검사의 적합성 그리고 오류…

## Slide 23: 적절성과 재현성

## Slide 24: C/C: Chronic cough
17/M
paroxysmal cough
at night with dyspnea
P/E: wheeze on
both lung field.
Case 3

## Slide 25: Reversibility
FEV1: 21% change after bronchodilator

## Slide 26: 1초당 노력 호기량 FEV1 변화량: 가역성

## Slide 27: 기도 가역성 검사

## Slide 28: 기도가역성

## Slide 29: hyperresponsiveness
환자
정상인
COPD 환자
기관지 수축제의 강도
기관지 반응정도

## Slide 30: 천식유발 검사: 과민성

## Slide 31: 기도 과민성
천식 확진
정상인
기도과민성
유발검사의 강도
기관지
반응정도

## Slide 32: 여러 기타 유형의 장애들

## Slide 33: 폐기능 장애의 유형들

## Slide 34: 상기도 폐쇄의 유형들

## Slide 35: Tracheomalacia: UOA

## Slide 36: 상기도 폐쇄의 유형들

## Slide 37: 기도삽관 후 기관 협착증

## Slide 38: 상기도 폐쇄의 유형들

## Slide 39: 하기도 폐쇄의 유형들

## Slide 40: 개원가에서 사용하는 폐기능 검사기
간이 폐기능 검사기 초소형 폐기능 검사기 호기 최대 유속 측정기

## Slide 41: PEF and PEFR
PEF is often used to monitor asthma symptoms, not COPD.
A simple Peak flow can help detect this sudden change in airways status.
In COPD, there are permannet changes to PEF and FEV1. So, using Peak Flow to detect sudden changes is COPD is not as effective as it is in measuring changes in Asthma

## Slide 42: PEF and COPD screening 기관지 확장제 선택의 팁
There are times when measuring PEF may be helpful.
people with poor peak flow, had poor spirometry consistent with COPD in 93% of the cases with FEV1 (below 60%).
PEF when used as a screening tool in undiagnosed people does a good job in predicting significant airways problems

## Slide 43: PEF & COPD mornitoring
A peak expiratory flow rate of less than 80% will detect more than 90% of people with chronic obstructive pulmonary disease in the community: <60% Pred.
Potential candidate for Bronchodilator treatment

## Slide 44: 핸드폰 의료기기의 시대

## Slide 45: 핸드폰 폐기능 측정기

## Slide 46: 경청해 주셔서 감사합니다 원격진료:폐기능 검사 지도 및 판독